## Slide 1: IE 324 SIMULATION
ARENA
BASIC OPERATIONS AND INPUTS

## Slide 2: Example
Consider the HW 2 question about the electronic assembly and test system

## Slide 3: PART I
What if there were two different parts with the following configuration?

## Slide 4: PART II
What if the processing times were different for each part at the sealer?

## Slide 5: PART III
What if we needed detailed statistics on the time in system per each exit?

## Slide 6: PART III
What if we needed detailed statistics on the time in system per each exit?
We will use the Record module (Only for Counter/Tally Statistics)
RECORD module options:
  Count (increase/decrease value of the statistic by the amount specified)
  Entity Statistics (save the recent entity statistics such as time/cost)
  Time Interval (Time between the current simulation time (TNOW) and the time saved as an attribute)
  Time Between (Time between two entities passing through the record)
  Expression (Value of the expression)

## Slide 7: PART IV
What if the resource capacity of the Rework station is 1 for 8 hours and 2 for the next 8 hours on a 16-hour workday?

## Slide 8: PART IV
What if the resource capacity of the Rework station is 1 for 8 hours and 2 for the next 8 hours on a 16-hour workday?
We will use schedule module to periodically change the resource capacity.
Schedule rules for capacity decrease:
  Preempt – Processing is interrupted, resumed at end of “break”
  Wait – Capacity decrease waits until entity releases Resource, and “break” will be full but maybe start/end late
  Ignore – Capacity goes down immediately for statistics collection*, but work goes on until finished … “break” could be shorter or gone

## Slide 9: PART V
What if the sealer machine breaks down for Expo(4) minutes after working for Expo(120) minutes?

## Slide 10: PART V
What if the sealer machine breaks down for Expo(4) minutes after working for Expo(120) minutes?
Failure module will change the resource state.
IDLE BUSY INACTIVE FAILED
(not seized) (seized) (no scheduled capacity)
Failure happens

## Slide 11: PART VI
Customized statistics collection via Statistics Module
Options:
  Time Persistent: Records the changes in the value of an expression throughout the simulation run and provides a time-average
  Tally
  Counter
  Output: Reports the final value (value at the end of the simulation run) of a given expression
  Frequency: Observes the value of an expression throughout the simulation run and reports the amount of time value of the expression is in a specified category.

## Slide 12: PART VI
Customized statistics collection via Statistics Module
Exercises:
  Find the average number of parts waiting in Part A and Part B Prep Areas combined.
  Find the number of parts in Sealer Process and Sealer Process Queue (i.e. total work in process) at the end of the simulation run
  Find the percentage of the time the rework queue has
    0 Parts
    (0,10] Parts
    (10,20] Parts
    (20,30] Parts
    (30,40] Parts

## Slide 13: PART VII
Part Transfers: Modify the model so that each transfer takes exactly 2 minutes between each station.